## Slide 1: The Imaging X-ray Polarimetry Explorer
Martin C. Weisskopf
NASA Marshall Space Flight Center
Presentation to APAC
March 15, 2021

## Slide 2
5.2 m total length
4.0 m focal length
Forward Star Tracker
Detector Unit (1 of 3)
Mirror Module Assembly (1 of 3)
IXPE Deployed

## Slide 3
IXPE Exists!
Janice Houston, IXPE Lead Systems Engineer
in residence at Ball, with stowed observatory

## Slide 4: The IXPE Team
SAT currently comprises > 90 scientists from 12 countries
Nagoya University Thermal Shields

## Slide 5: The Science Team
Investigators
  L. Baldini (Co-IPI), W. Baumgartner, R. Bellazzini, S. Bongiorno, E. Costa, J. Kolodziejczak, L. Latronico, H. Marshall, G. Matt, F. Muleri, S. O’Dell, B. Ramsey (DPI), R. Romani, P. Soffitta (IPI), A. Tennant, M. Weisskopf (PI)
Collaborators (75 from 12 countries)
  I. Aguido, L.A. Antonelli, M. Bachetti, S. Bianchi, R. Bonino, A. Brez, N. Bucciantini, F. Capitanio, E. Cavazzuti, E. Churazov, S. Ciprini, M. Cocchi, L. Costamante, A. De Rosa, E. Del Monte, N. Di Lalla, I. Donnarumma, V. Doroshenko, M. Dovčiak, S. Ehlert, T. Enoto, Y. Evangelista, S. Fabiani, J. Garcia, S. Gunji, K. Hayashida, J. Heyl, A. Ingram, W. Iwakiri, S. Jorstad, V. Karas, V. Kaspi, F. Kislat, T. Kitaguchi, H. Krawczynski, M. Kuss, I. Liodakis, G. Madejski, S. Maldera, A. Manfreda, F. Marin, A. Marinucci, A. Marscher, F. Massaro, I. Mitsuishi, T. Mizuno, S. Ng, N. Omodei, C. Oppedisano, L. Pacciani, A. Papitto, G. Pavlov, M. Perri, M. Pesce-Rollins, P.-O. PetruccI, M. Pilia, A. Possenti, J. Poutanen, S. Puccetti, M. Razzano, C. Sgrò, P. Slane, G. Spandre, L. Stella, R. Sunyaev, T. Tamagawa, F. Tavecchio, R. Taverna, Y. Tawara, N. Thomas, A. Trois, R. Turolla, J. Vink, K. Wu, S. Zane

## Slide 6: The Working Groups
Science Working Group (SWG)
  G. Matt (IT) & S. O’Dell (US), Co-Chairs
Science Advisory Team (SAT)
  G. Matt (IT) & R. Romani (US), Co-Chairs
SAT Topical Working Groups (TWG), Leads
  Pulsar Wind Nebula & Radio Pulsars, N. Bucciantini (IT)
  Supernova remnants, P. Slane (US)
  Accreting stellar-mass black holes, M. Dovčiak (CZ)
  Accreting neutron stars, J. Poutanen (FI)
  Magnetars, R. Turolla (IT)
  Radio-quiet AGN and Sgr A*, F. Marin (FR)
  Blazars & radio galaxies, A. Marscher (US)
Calibration Working Group
  W. Baumgartner (US), F. Muleri (IT), & J. Kolodziejczak (US)
Science Analysis & Simulation Working Group
  L. Baldini (IT) & H. Marshall (US)

## Slide 7: Shield and Collimator Suppress Background
X-ray
Shield
X-ray Shield
Detector Unit
On-axis Target
Mirror Module Assembly
Off-axis Background
Collimator

## Slide 8: Mirror-Shell Production Process
(+)
(+)
(-)
8. Separate shell from mandrel in chilled water
4. Polish mandrel to 0.3-0.4 nm RMS
7. Electroform Nickel/Cobalt shell onto mandrel
6. Passivate mandrel surface to reduce shell adhesion
3. Diamond turn mandrel to sub-micron figure accuracy
1. Machine mandrel from aluminum bar
5. Conduct metrology on the mandrel
2. Coat mandrel with electroless nickel (Ni-P)
Ni/Co electroformed IXPE mirror shell
Mirror-shell forming
Mandrel fabrication

## Slide 9: The Optics
Parameter | Value
Number of mirror modules | 3
Number of shells per mirror module | 24
Focal length | 4 m
Total shell length | 600 mm
Range of shell diameters | 162–272 mm
Range of shell thicknesses | 0.16–0.25 mm
Shell material | Electroformed nickel–cobalt alloy
Effective area per mirror module | 166 cm2 (@ 2.3 keV); > 175 cm2 (3–6 keV)
Angular resolution (HPD) | ≤ 27 arcsec
Field of view (detector limited) | 12.9 arcmin square
Front Spider Assembly
Outer Housing Tube
Rear Spider Assembly
X-ray Mirror Shells
Central Support Tube
MMA, showing 24 shells
MMA with Thermal Shield on end
Three IXPE Mirror Module Assemblies

## Slide 10: Stray Light Test Facility
X-ray calibration of the optics occurred at MSFC’s 100-m X-ray test facility
Mirror Module Assembly
X-Y stage with detector mounting plate

## Slide 11: Angular Resolution
MMA | #1 | #2 | #3
6.4 keV | 18.9″ | 24.8″ | 24.2″
4.5 keV | 18.9″ | 25.0″ | 26.9″
2.3 keV | 18.7″ | 24.5″ | 26.7″
Values in the table are half-power diameters (HPDs) for the individual MMAs alone. After adjustment for alignment errors, detector resolution, focus, etc., the on-orbit system-level resolution is 28″.
At-focus images for MMA1, MMA2 and MMA3 (left to right) taken at 2.3 keV, 4.5 keV and 6.4 keV (top to bottom).

## Slide 12: Imaging polarimetry
IXPE 30″ half-power diameter on Chandra image of the Crab Nebula

## Slide 13: Detection Principle
The detection principle is based upon the photoelectric effect
, where

## Slide 14: The Detector
Gas Pixel
Detector
Electronics
X Rays In
Collimator
The initial direction of the K-shell photoelectron is determined by the orientation of the incident photon’s electric vector
The distribution of the photoelectron initial directions measures the degree of polarization and the position angle

## Slide 15: Detector Properties
Parameter | Value
Sensitive area | 15 mm × 15 mm (13 x 13 arcmin)
Fill gas and asymptotic pressure | DME @ 0.656 atmosphere
Detector window | 50-µm thick beryllium
Absorption and drift region depth | 10 mm
GEM (gas electron multiplier) | copper-plated 50-µm liquid-crystal polymer
GEM hole pitch | 50 µm triangular lattice
Number ASIC readout pixels | 300 × 352
ASIC pixelated anode | Hexagonal @ 50-µm pitch
Spatial resolution (FWHM) | ≤ 123 µm (6.4 arcsec) @ 2 keV
Energy resolution (FWHM) | 0.57 keV @ 2 keV (∝ √E)
Useful energy range | 2 - 8 keV

## Slide 16: The Detectors
The Detectors mounted to the spacecraft top deck at Ball Aerospace

## Slide 17
Filter Calibration Wheel Assembly
Filter and Calibration Wheel (FCW), providing open, attenuated, and closed positions, plus four 55Fe-powered calibration sources:
  Cal A – Bragg-reflected polarized 2.98-keV (Ag-L𝛼 fluorescence) and 5.89-keV (Mn-K𝛼) Cal B – unpolarized 5.89-keV spot Cal C – unpolarized 5.89-keV flood Cal D – unpolarized 1.74-keV (Si-K𝛼 fluorescence) flood

## Slide 18: Minimum Detectable Polarization (MDP)
RS is the observed source counting rate
RB is the observed background counting rate
t is the integration time
M is the modulation factor—i.e., the amplitude of the variation of the ensemble of position angles for a 100%-polarized source

## Slide 19: Neural-Network Analysis
Baseline moments analysis is a simple, effective, long-studied and well-understood method of extracting information from ionization tracks made by the photo-electron in the detector gas
Machine Learning (neural-network) techniques can extract more information from each track
  Improves position-angle (PA) measurements, especially at higher energies
  Allows one to compute statistical and reconstruction errors for each event
  Mildly improves estimates of the energy and conversion point of each event

## Slide 20: First Year’s Mission — Release 1
Next version will be released 6 months prior to launch
Observing plan is from input from the IXPE Science Advisory Team
  Seven Topical Working Groups (TWG), based upon category of source
Needed exposure times assume moments-method event reconstruction
  Will increase somewhat, based upon results from recent calibration
However, neural-network event reconstruction will enhance the sensitivity
  Improves MDP99 by ~15% (relative) for fixed exposure time
  Reduces exposure time by ~30% for fixed MDP99
Source Category | # Sources | Time (Ms)
Pulsar Wind Nebulae | 3 | 2.6
Supernova Remnants | 3 | 3.0
Accreting Neutron Stars | 8 | 1.8
Accreting Black Holes | 2 | 0.6
Magnetars | 2 | 2.0
Radio Quiet AGN and Sgr A* | 4 | 2.8
Blazars and Radio Galaxies | 11 | 3.2
ToOs | 6 | 3
Total | 39 | 19

## Slide 21: Radio Pulsars
Radio Pulsars
  Perform X-ray phase-resolved polarimetry to test models for a radio pulsar’s X-ray emission
    Crab Pulsar — grey is optical, blue is IXPE
Emission geometry and processes are still unsettled.
Competing models predict differing polarization behavior with pulse phase.
X-rays provide a clean probe of geometry.
Absorption likely more prevalent in visible band.
Radiation process entirely different in radio band.
  Recently discovered no pulse phase-dependent variation in polarization degree and position angle @ 1.4 GHz.
140-ks observation of the Crab pulsar gives ample statistics to track polarization degree and position angle.

## Slide 22: Microquasars
Microquasars
  Perform X-ray spectral polarimetry on microquasars to use the position angle to help localize the emission site (accretion disk, corona, jet) and determine the spin
  For a microquasar in an accretion-dominated state, scattering polarizes the disk emission.
  Polarization rotation versus energy is greatest for emission from inner disk.
    Inner disk is hotter, producing higher energy X-rays.
  Disk orientation from other experiments may be used to constrain GRX1915+105 model.
    a = 0.50±0.04; 0.900±0.008; 0.99800±0.00003 (200-ks observation)

## Slide 23: Active Galaxies: Cen A
Active galaxies powered by supermassive black holes with jets
  Radio polarization implies the magnetic field is aligned with jet
  Different electron-acceleration models predict different dependences in X-rays
Region | MDP99
Core | 1.4%
Knots C+F+G | 21%
ULXs | 25%, 15%
ULX sources
Jet knots

## Slide 24: Test QED
Study magnetars (pulsing neutron stars with magnetic fields up to 1015 Gauss)
  Non-linear QED predicts magnetized-vacuum birefringence
    Refractive indices of the two polarization modes differ from 1 and from each other
    Impacts polarization and position angle as functions of pulse phase, but not the flux
    Example is 1RXS J170849.0-400910, with an 11-s pulse period
    Can exclude QED-off at better than 99.9% confidence in 250-ks observation

## Slide 25: Conclusion
    We are keenly looking forward to opening this new window on the sky by adding image resolved polarimetry to the arsenal of tools to study the X-ray emission from astrophysical sources.
    Scheduled launch date is 2021 November 17!